## Slide 1: Mobot Software Design Specification

## Slide 2: Block Diagram
PIC16F877A MCU
LEFT PROXIMITY SENSOR
LEFT PROXIMITY SENSOR
PORTB.B4
PORTB.B5
MOTOR DRIVE
PORTB.B3 / DIR_A
PORTB.B2 / DIR_B
CCP1 / PWM_A
CCP2 / PWM_B
MOTOR A/C
MOTOR B/D

## Slide 3: Microcontroller Unit
Device | PIC16F877A
Clock Speed | 20MHz
CPU | RISC
PWM | 2, 10 bits resolution
ROM | 8192 Words, 14.3KB
RAM | 368 bytes
I/O | 33, Ports A, B, C, D, E
No of pins | 40 Pin PDIP
# instructions | 35

## Slide 4: I/O Ports
PORTB is an 8-bit wide, bidirectional port. The corresponding data direction register is TRISB. Setting a TRISB bit (= 1) will make the corresponding PORTB pin an input (i.e., put the corresponding output driver in a High-Impedance mode). Clearing a TRISB bit (= 0) will make the corresponding PORTB pin an output (i.e., put the contents of the output latch on the selected pin).

## Slide 5: Setting and Clearing an Output Pin
We Set and Clear a Pin using PORTx by Masking.
Setting a Pin to High
Clearing a Pin to Low

## Slide 6: Pulse Width Modulator
PWM is a part of the CCP module. PWM1 is under CCP1 (RC2 Pin 17) and PWM2 is under (RC1 Pin 16) . PWM sets the Pulse width duration or Duty Cycle of a Square Wave.
Methods:
PWM1_Init(freq)
PWM1_Set_Duty(duty)
PWM1_Start()
PWM1_Stop()

## Slide 7: Modules
The Mobot is implemented in Finite State Machine.
Two Managers will be Implemented to modularize the Mobot.
Input Manager
  Manages the input sensor to set Mobot Input Sensing State.
  Input: Sensor1 and Sensor2 Logic. (High - Object Detected, Low – No Object Detected).
  Output: Input Sensing State
Motor Manager
  Manages the control of Motor Drive.
  Set and Clear Motor A and Motor B Direction(CW/CCW)
  Set PWM control for Motor Speed. (DC= 0%- OFF, DC = 20% - SLOW Movement, DC – 50% -Backward Movement, and 100% - Fast movement for Forward)
  Input: Input Manager Sensing State.
  Output: Motor A and Motor B Direction and PWM control for Motor Speed.

## Slide 8: Input Manager State Table
States | TASK | INIT | NO_SIGHT | LEFT_SIGHT | RIGHT_SIGHT | BOTH_SIGHT
INIT |  |  | NONE |  |  | 
NO_SIGHT |  |  |  | sensor1 and !sensor2 | !sensor1 and sensor2 | 
LEFT_SIGHT |  |  | !sensor1 and !sensor2 |  | !sensor1 and sensor2 | sensor1 and sensor2
RIGHT_SIGHT |  |  | !sensor1 and !sensor2 | sensor1 and !sensor2 |  | sensor1 and sensor2
BOTH_SIGHT |  |  | !sensor1 and !sensor2 | sensor1 and !sensor2 | !sensor1 and sensor2 | 

## Slide 9: Input Manager State Machine

## Slide 10: Motor Manager State Table
States | TASK | INIT | OFF | SLOW_LEFT | SLOW_RIGHT | FAST_FORWARD | BACKWARD | Delay
INIT |  |  | NONE |  |  |  |  | 
OFF | direction_a=A_CW , direction b = B_CCW, pwm_a =0, pwm_b =0 |  |  | [input]state = LEFT_SIGHT | [input]state = RIGHT_SIGHT |  | [input]state = RIGHT_SIGHT and [input]state = LEFT_SIGHT | 
SLOW_LEFT | direction_a = A_CCW , direction_b = B_CCW, pwm_a =20, pwm_b =20 |  |  |  | [input]state = RIGHT_SIGHT |  | [input]state = RIGHT_SIGHT and [input]state = LEFT_SIGHT | 
SLOW_RIGHT | direction_a = A_CCW , direction_b = B_CCW, pwm_a =20, pwm_b =20 |  |  | [input]state = RIGHT_SIGHT |  |  | [input]state = RIGHT_SIGHT and [input]state = LEFT_SIGHT | 
BACKWARD | direction_a = A_CCW , direction_b = B_CW, pwm_a =50, pwm_b =50 |  |  |  |  |  |  | NONE
DELAY | direction_a=A_CW , direction b = B_CCW, pwm_a =0, pwm_b =0, delay = 1sec , |  |  |  |  | delay |  | 
FAST_FORWARD | direction_a = A_CW , direction_b = B_CCW, pwm_a =100, pwm_b =100 |  | [input]state = NO_SIGHT |  |  |  |  | 

## Slide 11: Motor Manager State Machine

## Slide 12: Class Diagram